## Slide 1
Differentiable optimization for control and reinforcement learning
Brandon Amos
Meta AI NYC, Fundamental AI Research (FAIR)
Collaborators: Akshay Agrawal, Shane Barratt, Byron Boots, Stephen Boyd, Roberto Calandra, Steven Diamond, Priya Donti, Ivan Jimenez, Zico Kolter, Nathan Lambert, Jacob Sacks, Samuel Stanton, Andrew Gordon Wilson, Omry Yadan, and Denis Yarats
brandondamos
bamos.github.io
github.com/bamos/presentations
Slides available at:

## Slide 2: Control is powerful*
Setting: deterministic, discrete-time system with a continuous state-action space
Widely deployed over the past century for aviation, robotics, autonomous driving, HVAC
Often for a Markov decision process but doesn’t have to be
The real-world is non-convex, so are our controllers
Convex in some cases and subproblems, e.g., with quadratic cost/linear dynamics (LQR)
NO LEARNING NECESSARY if we know the system — just pure optimization
Notation: are the parameters of the controller (usually of the cost or dynamics)
*when properly set up
cost
dynamics
constraints
initial state
Full notation:

## Slide 3: Model-free RL and control
Take the cost to be the (negated) value estimate, no dynamics
Value estimate approximates the model-based objective
Policy learning performs amortized optimization
Viewpoint leads to a model-based to model-free spectrum:
take short-horizon model-based rollouts with a value estimate at the end
cost
dynamics
constraints
initial state
Full notation:

## Slide 4: Control may fail for many reasons
Control starts failing us when we can’t describe everything
Impossible to analytically encode every detail of non-trivial systems
Cost and dynamics may be unknown, mis-specified, or inaccurate
Especially difficult in high-dimensional state-action spaces
Learning methods help but are not perfect
system identification, learning dynamics, inverse cost learning
cost
dynamics
constraints
initial state
Full notation:

## Slide 5: Controllers don’t live in isolation
cost
dynamics
constraints
initial state
controller parameters
(design space of cost and model)
solve control optimization problem
execute control policy on the system
measure downstream performance of the controller
We can often measure the downstream performance induced by the controller
Idea: optimize (i.e., tune/learn) the parameters for a downstream performance metric
Controller-design loop is not a new idea and has been extensively used over the past century
Full notation:

## Slide 6: This talk: differentiate the controller!
differentiable control
We can often measure the downstream performance induced by the controller
Idea: optimize (i.e., tune/learn) the parameters for a downstream performance metric
by differentiating through the control optimization problem
or
cost
dynamics
constraints
initial state
controller parameters
(design space of cost and model)
solve control optimization problem
execute control policy on the system
measure downstream performance of the controller
Full notation:

## Slide 7: This talk: differentiate the controller!
Foundations of differentiable optimization and control
Unrolling or autograd (gradient descent, differentiable cross-entropy method)
Implicit differentiation (convex and non-convex MPC)
cvxpylayers: Prototyping differentiable convex optimization and control
Applications of differentiable control
Objective mismatch
Amortized control

## Slide 8: Derivatives in RL and control
Each vertical slice is a control problem
The policy (or value) gradient Derivative of value w.r.t. a parameterized policy:
For policy learning via amortized optimization
-value can be model-based or model-free
Works for deterministic and stochastic policies
Differentiable control — this talk
Derivative of actions w.r.t. controller parameters:
Controller induces a model-based policy

## Slide 9: How to differentiate the controller?
Implicit differentiation
Idea: Differentiate controller’s optimality conditions
Agnostic of the control algorithm
Ill-defined if controller gives suboptimal solution
Memory and compute efficient: free in some cases
Unrolling or autograd
Idea: Implement controller, let autodiff do the rest
Like MAML’s unrolled gradient descent
Ideal when unconstrained with a short horizon
Does not require a fixed-point or optimal solution
Instable and resource-intensive for large horizons
Can unroll algorithms beyond gradient descent
The differentiable cross-entropy method

## Slide 10: How to differentiate the controller?
Implicit differentiation
Idea: Differentiate controller’s optimality conditions
Agnostic of the control algorithm
Ill-defined if controller gives suboptimal solution
Memory and compute efficient: free in some cases
Unrolling or autograd
Idea: Implement controller, let autodiff do the rest
Like MAML’s unrolled gradient descent
Ideal when unconstrained with a short horizon
Does not require a fixed-point or optimal solution
Instable and resource-intensive for large horizons
Can unroll algorithms beyond gradient descent
The differentiable cross-entropy method

## Slide 11: The Differentiable Cross-Entropy Method (DCEM)
The cross-entropy method (CEM) optimizer:
1. Samples from the domain with a Gaussian 2. Updates the Gaussian with the top-k values
Solves challenging non-convex control problems
The differentiable cross-entropy method (DCEM):
Use unrolling to differentiate through CEM using:
1. the reparameterization trick for sampling
2. a differentiable top-k operation (LML)

## Slide 12: From the softmax to soft/differentiable top-k
Constrained softmax, constrained sparsemax, Limited Multi-Label Projection
Has closed-form solution
No closed-form solution, can still differentiate
Entropy penalty of the softmax
top-k polytope

## Slide 13: How to differentiate the controller?
Implicit differentiation
Idea: Differentiate controller’s optimality conditions
Agnostic of the control algorithm
Ill-defined if controller gives suboptimal solution
Memory and compute efficient: free in some cases
Unrolling or autograd
Idea: Implement controller, let autodiff do the rest
Like MAML’s unrolled gradient descent
Ideal when unconstrained with a short horizon
Does not require a fixed-point or optimal solution
Instable and resource-intensive for large horizons
Can unroll algorithms beyond gradient descent
The differentiable cross-entropy method

## Slide 14: The Implicit Function Theorem
Given an implicit function defined by where
How can we compute ?
The Implicit Function Theorem gives under mild assumptions
Dini 1877, Dontchev and Rockafellar 2009
Contour of defining an implicit function
Each vertical slice is a control problem

## Slide 15: Implicitly differentiating convex LQR control
Backward pass: implicitly differentiate the LQR KKT conditions:
where
Just another LQR problem!
Parameters:
Define implicit function via KKT optimality conditions
Find s.t. where
Solved with Riccati recursion

## Slide 16: Differentiating non-convex MPC
Backward pass: differentiate the convex approximation, e.g., with:
where
Just an LQR problem! (in some cases)
Solve with sequential quadratic programming (SQP)
Approximate non-convex argmin with the final convex approximation
cost
dynamics
constraints
initial state

## Slide 17: This talk: differentiate the controller!
Foundations of differentiable optimization and control
Unrolling or autograd (gradient descent, differentiable cross-entropy method)
Implicit differentiation (convex and non-convex MPC)
cvxpylayers: Prototyping differentiable convex optimization and control
Applications of differentiable control
Objective mismatch
Amortized control

## Slide 18: Optimization layers need to be carefully implemented

## Slide 19: Why should practitioners care?

## Slide 20: Differentiable convex optimization layers
NeurIPS 2019 and officially in CVXPY!
Joint work with A. Agrawal, S. Barratt, S. Boyd, S. Diamond, J. Z. Kolter
Useful for convex control problems and subproblems
locuslab.github.io/2019-10-28-cvxpylayers

## Slide 21: Rapidly prototyping optimization layers

## Slide 22: Code example: OptNet QP
Before: 1k lines of code Hand-implemented and optimized PyTorch GPU-capable batched primal-dual interior point method
Now: <10 lines of code Same speed
Write standard CVXPY problem
Export to PyTorch, TensorFlow, JAX

## Slide 23: Under the hood: cone program differentiation
Find s.t. where and
Implicitly differentiating gives
Section 7 of my thesis and in Agrawal et al.
Conic Optimality

## Slide 24: This talk: differentiate the controller!
Foundations of differentiable optimization and control
Unrolling or autograd (gradient descent, differentiable cross-entropy method)
Implicit differentiation (convex and non-convex MPC)
cvxpylayers: Prototyping differentiable convex optimization and control
Applications of differentiable control
Objective mismatch
Amortized control

## Slide 25: The Objective Mismatch Problem
Summary: Maximum-likelihood training of dynamics separate from controlling the dynamics
Especially problematic with inaccurate models
The controller (i.e. policy) optimizes over the dynamics
Can find adversarial trajectories that appear deceptively “good”
Differentiable control one potential solution, may be combined with many others:
advantage weighting, value-gradient weighting, value-aware model learning

## Slide 26: Optimizing the task loss is better than SysID
True System: Pendulum environment with noise (damping and a wind force) Approximate Model: Pendulum without the noise terms
True Model
Approximate Model Class
Best Imitation Loss
Best MSE
~1.8x difference!

## Slide 27: Optimizing system models with a task loss
Among many others!

## Slide 28: This talk: differentiate the controller!
Foundations of differentiable optimization and control
Unrolling or autograd (gradient descent, differentiable cross-entropy method)
Implicit differentiation (convex and non-convex MPC)
cvxpylayers: Prototyping differentiable convex optimization and control
Applications of differentiable control
Objective mismatch
Amortized control

## Slide 29: RL policy learning is amortized optimization
Setup: controlling a continuous MDP with a model-free policy
Review: Learning a policy with a value gradient amortizes over the -value:
is fully amortized: tries to predict the max- operation without looking at the function!
The amortization perspective easily enables us to consider other policies

## Slide 30: Amortized control via unrolled gradient descent
The policy’s prediction is adapted to maximize the function for every state
Unrolled gradient descent: policy has knowledge it is going to be adapted
Can generalize to other differentiable optimizers, e.g., the cross-entropy method

## Slide 31: Optimal control sequences share structure
Control optimization problems are repeatedly solved for every state
Optimal control sequences do not live in isolation and share structure
Use differentiable control to learn a latent subspace
Only search over optimal solutions rather than the entire space
Amortizes the original control optimization problem
Optimal controls over time — force on the cartpole
Time
Full control sequence space
Subspace of optimal solutions
Cartpole videos

## Slide 32: DCEM learns the solution space structure
Full control sequence space
Subspace of optimal solutions
Latent space of optimal solutions

## Slide 33: Closing Thoughts And Future Directions
Differentiable optimization and control are powerful primitives to use within larger systems
Theoretical and engineering foundations are here
Works for convex and non-convex control
Specify and hand-engineer the parts you know, learn the rest
Can be propagated through and learned, just like any layer
Applications in:
Objective mismatch
Amortized optimization
Safe and robust control
Learning state embeddings

## Slide 34
Differentiable QPs: OptNet [Amos and Kolter, ICML 2017]
Differentiable task-based stochastic optimization [Donti, Amos, Kolter, NeurIPS 2017]
Differentiable MPC for end-to-end planning and control [Amos, Jimenez, Sacks, Boots, Kolter, NeurIPS 2018]
Differentiable Convex Optimization Layers [Agrawal*, Amos*, Barratt*, Boyd*, Diamond*, Kolter*, NeurIPS 2019]
Differentiable optimization-based modeling for ML [Amos, Ph.D. Thesis 2019]
Differentiable Cross-Entropy Method [Amos and Yarats, ICML 2020]
Objective mismatch in model-based reinforcement learning [Lambert, Amos, Yadan, Calandra, L4DC 2020]
On the model-based stochastic value gradient [Amos, Stanton, Yarats, Wilson, L4DC 2021]
Tutorial on amortized optimization [Amos, arXiv 2022]
Differentiable optimization for control and reinforcement learning
Brandon Amos
Meta AI NYC, Fundamental AI Research (FAIR)
brandondamos
bamos.github.io
Collaborators: Akshay Agrawal, Shane Barratt, Byron Boots, Stephen Boyd, Roberto Calandra, Steven Diamond, Priya Donti, Ivan Jimenez, Zico Kolter, Nathan Lambert, Jacob Sacks, Samuel Stanton, Andrew Gordon Wilson, Omry Yadan, and Denis Yarats
github.com/bamos/presentations
Slides available at: