## Slide 1
There are a lot of model-based priors for reinforcement learning:
Among others: Dyna-Q (Sutton, 1990), GPS (Levine and Koltun, 2013), Imagination-Augmented Agents (Weber et al., 2017), Value Iteration Networks (Tamar et al., 2016), TreeQN (Farquhar et al., 2017) Hindsight Plan (Tamar et al., 2017)
These typically involve:
Using an RNN: Efficient but not as expressive and general as MPC/iLQR
Unrolling an LQR or gradient-based solver: Expressive/general but inefficient
Differentiable MPC for End-to-End Planning and Control
https://locuslab.github.io/mpc.pytorch https://github.com/locuslab/differentiable-mpc
Introduction and Motivation
Model-free RL
More general, doesn’t make as many assumptions about the world
Rife with poor data efficiency and learning stability issues
Model-based RL (or control)
A useful prior on the world if it lies within your set of assumptions
Combining model-based and model-free reinforcement learning (RL) methods is important to get the best of both methods.
We propose to combine them with a differentiable control layer that can be backpropagated through like any other layer
Given: Expert trajectories from a hand-crafted controller
Goal: Reconstruct missing parts (cost and dynamics) of the controller with imitation learning given only nominal trajectories
Loss:
In a domain where the true model class is unrealizable, traditional system identification (SysID) may not be the best if you know the task that you want to use control for. Instead, directly optimizing the task loss is better.
We show this in a pendulum domain where the true model has noise terms (damping and wind)
Brandon Amos1 • Ivan Dario Jimenez Rodriguez2 • Jacob Sacks2 • Byron Boots2 • J. Zico Kolter13
1Carnegie Mellon University • 2Georgia Tech • 3Bosch Center for AI
Model Predictive Control
Imitation Learning Experiment: LQR
Should RL policies have a systems dynamics model or not?
Our Contribution: A Differentiable Control Layer
We consider non-convex control optimization problems, expanding the scope of OptNet layers
Where can these be used? These differentiable control layers can be integrated as part of the policy class in model-free algorithms or imitation learning. Unrolled controllers can be replaced with this.
Imitation Learning Experiments: Pendulum and Cartpole
Imitation Learning Experiments: Unrealizable Pendulum
Related Work: Combining model-based and model-free RL
Given: Expert trajectories from a hand-crafted controller
Goal: Reconstruct missing parts (dynamics) of the controller with imitation learning given only nominal trajectories
Loss: where
A widely-used powerhouse of modern control. Typically solved with sequential quadratic programming, an iterative method that forms convex quadratic approximations to the problem.
LQR, KKT Systems, and Differentiation
Linear-Quadratic Regulator (LQR): A special case of MPC that is convex with a quadratic cost and linear dynamics. Solving LQR with the Riccati recursion efficiently solves the KKT system
Backwards Pass: Use the OptNet approach from [Amos and Kolter, 2017] to implicitly differentiate LQR:
where
Differentiating MPC: If a fixed-point is reached, then differentiate through the corresponding convex approximation.
Our standalone differentiable MPC solver: https://locuslab.github.io/mpc.pytorch
(Just an LQR solve!)
(8)
Solves (10), executes the first action on the system, and repeats.
(10)